## Slide 1
Department of Electrical and Computer Engineering
    Computer Engineering 186
    Spring 2019
Alexis J. Renderos, William Lavelle, Rolf Anderson, Ritvik Maripally
Acknowledgements
Adaptive Visual Target Identification and Tracking through
Convolutional Neural Network (CNN) based Machine Learning and Computer Vision
Abstract
The aim of this project is to identify a chosen object of interest at range using a camera feed and an image processing algorithm to assist in the detection, identification and tracking of the target. This solution was then implemented as a rail-mounted tactical scope attachment for a Nerf Blaster. The attachment provides the user with real-time feedback regarding their current
INPUT
CONVOLUTION + RELU POOLING
CONVOLUTION + RELU POOLING …
FULLY
CONNECTED
FLATTEN
SOFTMAX
CLASSIFICATION
FEATURE LEARNING
Target Detection and Identification
Target identification is primarily achieved through the implementation of a machine learning based algorithm. A Convolutional Neural Network (CNN) was trained on a dataset of nearly 3,000 photos of the three targets in order to create a comprehensive profile of what the targets looked in the eyes of a digital camera. The resulting model was then used to analyze incoming camera data to locate and identify any potential targets in its field of view.
Target Tracking
Target tracking is accomplished using a hybridized algorithm known as KCF, or Kernelized Correlation Filters. We chose this algorithm due to its high speed, exceptional accuracy, and excellent failure detection. Unfortunately, KCF does not recover well from full occlusion, but the target tracking algorithm is able to recover from this by implementing the aforementioned target identification algorithm.
Data Collection and Analysis
To properly analyze incoming image data, we must first determine the characteristics of our target. The three chosen targets (Fig. 1) were photographed over 1,000 times each in varying lighting conditions and at varying angles and varying degrees of occlusion. This provided us with a set of testing data and training data for our machine learning algorithm. We also analyzed the colors and markings of the targets in addition to the angle of the target relative to the camera and the lighting conditions. This was later used to create an object recognition and tracking algorithm.
Implementation
The aim of this project is to identify a chosen object of interest at range using a camera feed and an image processing algorithm to assist in the detection, identification and tracking of the target. It is expected that the object of interest has already been analyzed prior to identification attempts, and that the target is in the field of view of the camera.
Conclusion and Analysis
Overall, the CNN based algorithm performed equally in comparison to the purely algorithmic solution. We found that the CNN algorithm had no trouble with identification but struggled heavily when faced with target occlusion. In contrast, the algorithmic solution excelled at recovering from occlusion, but struggled with target identification in extreme light conditions. We believe that with enough training data and training time/epochs that the CNN algorithm will overtake the success of the algorithmic solution.